## Slide 1: Introduction to Computer Systems
Department of Computer Science and Information Systems
Lecturer: Steve Maybank
sjmaybank@dcs.bbk.ac.uk
Spring 2020
Week 2b: Storing Integers

## Slide 2: Representations of Negative Integers
Put a minus sign in front of the representation for a positive integer.
Excess notation.
Two’s Complement notation – the most popular representation for integers in computers.

## Slide 3: Excess Notation
Problem: represent a set of positive and negative integers using bit strings with a fixed length n
Represent 0 by 10…0 (n bits)
Represent positive numbers by counting up from 10…0 in standard binary notation
Represent negative integers by counting down from 10…0 in standard binary notation.

## Slide 4: Three Bit Excess Notation
n=3
111 3
110 2
101 1
100 0
011 -1
010 -2
001 -3
000 -4

## Slide 5: Alternative Name: Excess Four Notation
bit string = Binary(number+4)
e.g.
110 = Binary(2+4)
011 = Binary(-1+4)
111 3
110 2
101 1
100 0
011 -1
010 -2
001 -3
000 -4

## Slide 6: Examples
Find the 6 bit excess notation for the decimal numbers 7 and -6.
Which decimal number has the 5 bit excess notation 10101?

## Slide 7: Two’s Complement Notation
bit two’s complement notation for integers in the range
Eg.

## Slide 8: More Examples

## Slide 9: Example of Two’s Complement Notation
0111 7
0110 6
0101 5
0100 4
0011 3
0010 2
0001 1
0000 0
1111 -1
1110 -2
1101 -3
1100 -4
1011 -5
1010 -6
1001 -7
1000 -8
n=4
The left most bit indicates the sign.

## Slide 10: Addition and Subtraction
In the two’s complement system subtraction reduces to addition.
E.g. to evaluate 6-5 in 4 bit two’s complement notation, add the tc bit strings for 6 and –5, then take the four rightmost bits.
0110 6
1011 -5
=== ==
10001 1

## Slide 11: Explanation
TC(6) = rightmost four bits of Binary(24+6)
TC(-5) = rightmost four bits of Binary(24-5)
Binary((24+6)+(24-5))= Binary(24+24 +1).
The right most four bits of Binary(24+24 +1) form the bit string for TC(1).

## Slide 12: Why Use Two’s Complement
Addition and subtraction require one circuit for addition and one circuit for negation.
This is more efficient than having a circuit for addition and a circuit for subtraction.

## Slide 13: Notation
Let s, t be bit strings. The concatenation of s and t is s||t, e.g.
110||001 = 110001
Let s be a bit string. Then complement(s) is the bit string obtained by reversing the bits of s, e.g.
complement(110) = 001

## Slide 14: Two’s Complement Notation for m and -m
Let TC(m) = s || 1 || t, where t is a string of zeros
TC(-m) = complement[s]||1||t.
Examples: n = 4,
TC(3) = 0011, TC(-3) = 1101
TC(-1) = 1111, TC(1) = 0001

## Slide 15: TC(m) and TC(-m)
TC(m) = rightmost bits of
TC(-m) = rightmost bits of
TC(m)+TC(-m) = rightmost bits of
Therefore
TC(m)+TC(-m) = 0 =TC(0) = TC(m-m)

## Slide 16: Expression for TC(-m)
Let TC(m) = s || 1 || t, where t is a string of zeros.
To prove TC(-m) = complement(s)||1||t, show that
s||1||t + complement(s)||1||t = 0
t+t = t = string of zeros
1+1 = 0+carry
s+complement(s) = string of ones
carry+string of ones = 10…0
The rightmost n bits are all zero.

## Slide 17: Alternative Expression
TC(-m) = complement(TC(m))+1
Proof: let r be a string of 1s with the same length as t. Then
complement(s||1||t)+1=(complement(s)||0||r)+1
= complement(s)||1||t

## Slide 18: Two’s Complement and Subtraction
Subtraction can be carried out using addition
and the two’s complement notation TC. This
reduces the complexity of the circuits required
for arithmetic
(correct for the rightmost n bits only)

## Slide 19: Example
Find the 5 bit two’s complement representations for the decimal integers 5 and -5.